## Slide 1
CATERPILLAR HACKATHON · PROBLEM STATEMENT
Dump Packing is Broken
for Autonomous Mines
Autonomous trucks achieve less than half the packing
density of staffed operations — and current planning
tools make it worse, not better.
2-Step
Current planning process
Fill spots → plan lanes. Both steps are manual.
7.38m
Autonomous dump spacing (observed)
From satellite imagery of active autonomous mine
3.03m
Staffed operation spacing (observed)
From satellite imagery of staffed mine operations
~2.4×
Density gap to close
(7.38÷3.03)² ≈ area ratio — the real target
Root Causes of the Density Gap:
Small trucks overshoot pre-defined spot points → low spots / depressions form
Irregular polygon edges always leave uncovered dead zones with fixed grid spots
Mixed fleets (different payload sizes) cannot share the same spot-point plan
Prior dump piles detected as obstacles → trucks stop short, widening gaps
No arrival-sequence guidance → trucks block each other, causing respot cycles
01 / 07

## Slide 2
OUR SOLUTION
Adaptive Polygon Packing — Three Phases of Ambition
We propose a phased solution. Phase 1 is our hackathon deliverable — provably implementable. Phases 2 & 3 are the roadmap.
PHASE 1 · HACKATHON MVP
Optimised Polygon
Spot-Point Packing
A geometric algorithm replaces fixed pre-defined grids with a dynamically computed staggered/radial fill pattern fitted to the exact dump polygon boundary. Works for any irregular shape. Handles standard single-fleet trucks. Lanes may still be pre-planned to each generated spot.
Solvable with classical computational geometry
No truck hardware changes required
Simutable & demonstrable today
Directly closes the density gap
★ CORE PROPOSAL
PHASE 2 · NEAR-TERM ROADMAP
Dynamic Lane-Free
Mixed-Fleet Planning
Static spot points are replaced with a real-time dump plan updated as trucks arrive. Each truck's payload is used to size its zone dynamically. Mixed fleets can share one dump without manual re-planning. Requires reliable V2X communication.
Handles payload-variable fleets
Eliminates manual re-planning
Requires V2X comms investment
~18–24 months to field trial
FUTURE VISION
PHASE 3 · LONG-TERM VISION
Perception-Driven
Fully Autonomous Planning
No pre-defined plan at all. Trucks use onboard LiDAR + semantic segmentation to detect existing piles, self-assign spot points, and coordinate via peer-to-peer messages. Maximum flexibility, highest engineering complexity.
Zero infrastructure dependency
Works in GPS-denied areas
Highest R&D investment needed
3–5 year horizon realistically
RESEARCH STAGE
02 / 07

## Slide 3
PHASE 1 — HOW IT WORKS
Optimised Polygon Spot-Point Packing — Detailed Algorithm
01
Polygon Boundary Ingestion & Validation
The dump boundary is input as a geo-referenced polygon (GPS coordinates). The algorithm validates convexity, computes the minimum bounding rectangle, and identifies edge segments. Truck turning radius (e.g. CAT 793 = ~12m) defines a mandatory inset buffer — no spot point may be placed within this inset of the polygon edge.
02
Polygon Decomposition into Fill Zones
For irregular (non-convex) polygons, the boundary is decomposed into convex sub-polygons using standard ear-clipping or Hertel-Mehlhorn decomposition. Each convex zone is filled independently. This is the key step that eliminates dead zones — every zone is fully coverable by a regular pattern.
03
Staggered Grid Generation & Density Optimisation
Within each convex zone, a staggered hexagonal close-packing grid is generated. Spot-point spacing equals truck body width + safety margin (configurable per truck class). The grid orientation is optimised by testing rotations in 5° increments and selecting the angle that maximises the count of valid (inset-respecting) spot points. This is a deterministic O(n) search.
04
Lane Assignment & Arrival Sequencing
Spot points are grouped into approach lanes based on the primary truck ingress direction. Within each lane, points are sequenced nose-to-tail to prevent trucks crossing paths. A simple greedy scheduler assigns arriving trucks to the next available spot in the nearest lane. Deadlock is prevented by enforcing one-truck-per-lane-segment at a time — no complex coordination required.
05
Pile Proximity Check (Optional Enhancement)
If truck perception data is available, generated spot points are filtered against a live pile map. Any spot point whose centre falls within 1.5× pile radius of an existing pile is shifted to the nearest valid position or removed. This is an optional add-on — the core algorithm works without it, making it independently deployable.
03 / 07

## Slide 4
NOVELTY
What's Actually New Here
We are not inventing new geometry — we are applying it in a context where it has never been systematically used.
Dimension
Today's Approach
Our Phase 1 Approach
Why It Matters
Polygon coverage
Fixed rectangular grid — irregular edges always missed
Convex decomposition + per-zone fill — 100% coverage guaranteed
Eliminates dead zones that require dozer reshaping
Pattern geometry
Staggered rows manually tuned by operator
Hexagonal close-pack auto-computed — provably maximum 2D density
~9% denser than square grid — directly measurable
Shape adaptability
Same spot-point template reused regardless of dump shape
Grid orientation optimised per polygon — rotated to best fit
No wasted boundary space for irregular paddocks
Truck radius aware
Turning radius not encoded in spot point placement
Mandatory inset buffer = truck turning radius, hard-coded per model
Trucks never need to reverse or respot near edges
Fleet handling
Single truck class assumed; mixed fleets break the plan
Phase 1: single class (honest limitation); Phase 2 extends this
Honest scoping — we don't over-claim Phase 1
04 / 07

## Slide 5
SCALABILITY
What Scales Easily, What Requires Work, and What Has Limits
Scales Well ✔
Dump polygon size
Algorithm complexity is O(n·k) in polygon vertices and spot count — runs in milliseconds even for 100-point polygons.
Number of sequential trucks
The lane sequencer adds one assignment per truck arrival. No combinatorial explosion. Works for 2 to 500+ trucks over a dump's lifetime.
Different dump shapes
Convex decomposition handles any simple polygon. Works for rectangular pads, L-shapes, wedges, and fan-shaped paddocks equally.
Simulation & testing
Algorithm is entirely deterministic — unit-testable, reproducible, and simulatable offline before any field deployment.
Scales With Investment ⚠
Multiple concurrent trucks
Greedy lane scheduler works for 2–4 trucks with simple exclusion zones. Beyond that, a proper multi-agent scheduler is needed.
Mixed payload fleets
Requires dynamic zone resizing per payload class. Needs payload telemetry from each truck. Phase 2 scope.
Site-to-site deployment
Algorithm is portable, but integration with each site's fleet management system requires separate API work per site.
Pile detection integration
Works modularly, but requires semantic segmentation model training per mine's soil type and LiDAR configuration.
Honest Limitations ✗
3D dump surface topology
Phase 1 treats the dump as a flat 2D polygon. Actual dumps develop uneven surfaces — spot points may shift on sloped areas.
Real-time dynamic replanning
Phase 1 generates a static plan before the dump starts. Dynamic mid-dump replanning requires Phase 2 architecture.
Non-contiguous dump zones
If trucks deposit material creating internal obstacles mid-dump, Phase 1 cannot re-route around them dynamically.
GPS-denied environments
Algorithm assumes accurate truck positioning. Poor GPS in deep cuts or under canopy reduces spot-point accuracy.
05 / 07

## Slide 6
FEASIBILITY
Honest Technology Readiness & Realistic Deployment Timeline
Technology Readiness by Component
Polygon packing algorithm
Mature — used in PCB layout, robotics path planning
TRL 8
Truck turning radius model
Already in CAT Command for Hauling platform
TRL 9
Convex decomposition
Standard computational geometry — open source libs exist
TRL 8
Lane greedy scheduler
Proven concept in AGV systems; mine-specific tuning needed
TRL 6
Semantic pile segmentation
Achievable with LiDAR+camera; needs mine-specific training data
TRL 4
Multi-truck dynamic replanning
Research stage — complex distributed systems problem
TRL 3
Realistic Deployment Roadmap
Months 0–3
Algorithm Development
Build & validate packing algorithm in simulation. Input: polygon + truck spec. Output: spot-point map. Measurable KPI: density vs grid baseline.
Months 3–6
Single-Truck Field Validation
Deploy on one CAT 793 at a test site. Compare observed spacing vs algorithm predictions. Calibrate inset buffer for real-world GPS noise.
Months 6–18
Multi-Truck Pilot (2–4 trucks)
Extend lane scheduler to handle concurrent trucks. Field trial at partner mine. Target: match staffed density ±15%. Regulatory safety review.
Months 18–36
Production Integration
Full integration with CAT Command for Hauling API. Rollout to 5–10 mine sites. Continuous improvement loop using telemetry feedback.
Year 3–5
Phase 2: Mixed Fleet (Separate scope)
Only begin after Phase 1 production data validates core algorithm. Requires V2X comms investment and payload telemetry on all trucks.
06 / 07

## Slide 7
BUSINESS PROSPECTS
The Commercial Case — Grounded in Real Numbers
7.38m → 3.03m
Target spacing reduction
(observed data, same mine site)
~$6B
Autonomous mining equipment
market by 2030 (Allied Market Rsrch)
100+ sites
Active autonomous mines globally
(CAT Command deployed)
$0 HW cost
Phase 1 is pure software —
no sensor upgrades needed
For Caterpillar
Revenue stream
New software licensing module for Command for Hauling — deployable to existing customer base with no hardware change.
Competitive moat
Density algorithm is patentable. Rivals (Komatsu AHS, Wenco) use fixed spot-point approaches today.
Data flywheel
Each mine deployment generates real spacing vs telemetry data — improves algorithm over time across fleet.
Upsell path
Phase 1 validates the platform for Phase 2 V2X comms and Phase 3 perception upgrades — larger ticket items.
For Mine Operators
Smaller dump footprint
Higher packing density → same tonnage in less area → reduced land rehabilitation liability at mine closure.
Fewer dozer passes
Current autonomous dumps need dozer reshaping to fix low spots. Dense packing eliminates most of this.
Extended dump life
Denser packing means more tonnes per acre → dump reaches capacity later → defers CAPEX on new dump construction.
Fuel & idle savings
Precise spot-point guidance reduces truck respot cycles — each respot costs ~3–5 minutes of idle fuel burn.
Risks to Acknowledge
GPS accuracy
Algorithm assumes ±0.3m positioning. Current autonomous trucks typically achieve ±0.5m — calibration needed.
Safety certification
Any change to truck path planning requires OHS/site safety review — adds 6–12 months before field deployment.
Operator buy-in
Mine site operators are conservative. Proving density gain in simulation before field trial is critical for adoption.
Competitive response
Komatsu and others will observe any CAT deployment — first-mover window is 12–18 months before parity.
07 / 07